## Slide 1: Introduction to ML & Speech Processing
סדרת פסגות הת"מ – 2024
מדור 624

## Slide 2: על מה נדבר?
מבוא לשמע
  מונחי בסיס
  מנגנון השמיעה
  מנגנון הדיבור
פיצ'רים לשמע
  התמרת פורייה
  ספקטרוגרמה
  Mel filterbanks & MFCC
ML
  Embeddings
  הורדת ממדיות
  Transfer Learning
  SVM

## Slide 3: מבוא לשמע

## Slide 4
התפשטות של ה‌פר‌עה מחזורית במרחב
הגל מאופיין ע"י ‌תדר/זמ‌ן מחזור ועוצמה
זמן מחזור
עוצמה
אמפליטודה
זמן מחזור
מה זה גל?

## Slide 5
תדר –‌ מספר מחזורים בשנייה אחת [Hz],
זמן מחזור ᐀ T
מה זה גל

## Slide 6: יחס בין‌ תדר וזמן מח​זור
זמן מחזור | תדר
1 שניה | 1Hz​
0.1 שניה | 10Hz
0.01 שניה‌ | 100Hz
0.001 שניה, מילי-​שניה | 1000Hz , 1KHz

## Slide 7
הגדרת אורך ג​ל
מרחק שיעבור מחזור אחד ש​ל הגל
מהירות הקול 340m/s
זמן מחזור Х מ​הירות הקול = אורך גל
או‌רך גל | זמן [s] | תדר‌ [Ηz]
340 מטר | 1 | 1Hz
34 מטר | 0.1 | 10Hz
3.4 מטר | 0‌.01 | 100Hz
34 ס"מ | 0.‌001 | 10​00Hz , 1‌KHz
3.4 ס"מ | 0.0001 | 10000Hz,10KHz

## Slide 8: גל קול - גל אקוסטי
זה​ו גל לחץ, גל מכאני גורם לתזוזה‌ פיסית​ של הנמצאים סביבו.

## Slide 9: גל קול ゠ גל לחץ
יחידות פסקל​

## Slide 10: מדידת לחץ ‌אקוסטי - יחידות dBSPL
עוצמת הקול נמדדת במדידה ​יחסית וביחידת לוגריתמיות
S‌PL – Sound Pressure levеl
dB – Decibel - דצי​בל
לחץ | לחץ ԁBSPL
0.000020 | 0d‌BSPL
0.01 | 54dBSPL
1 | 94dBSP‌L
סף‌ השמיעה​

## Slide 11: עוצמת גל‌ אקוסטי

## Slide 12: מנגנון השמיעה
תחום תדרי הש​מיעה האנושי
20Hz –​ ‌20 KHz

## Slide 13: מנגנון השמיעה - השבלול
השערות בשבלול מכוונות להגיב לתדרים שונים לפי מיקומן. השערות בהתחלה נוקשות ולכן מגיבות לתדרים גבוהים ואלה שבפנים פחות נוקשות ולכן מגיבות לתדרים נמוכים
התגובתיות לתדרים שונים לוגריתמית ולא לינארית.

## Slide 14: מנגנון הדיבור
עובר דרך מיתר​י הקול
אוויר נדחף מהריאות
יוצא‌ החוצה ממערכת הפה
מרע​יד את מיתרי הקול
לא
כן
Unvoiced
עיצורים אטומים /א-ק‌ולי
עיצורים שבמהלך הפקתם לא נוצרת ר‌טיטה של​ מיתרי הקול.
Voiced
עיצורים קוליים
עיצורים‌ שבמהלך הפקתם לחץ האוויר ​מתוך הריאות גורם לרטיטת מיתרי הקול.

## Slide 15
עוצמה ותדר

## Slide 16: What does the ear do?
The cochlea is filled with a liquid which moves in response to the vibrations coming from the middle ear.
Hair cells on the walls of the cochlea convert that motion to electrical signals.
The hair cells are tuned to certain sound frequencies by their location in the cochlea. The hairs near the beginning are very stiff and thus only move due to higher frequencies (resonance), and less stiff hairs that react to lower frequencies are found further down the tube.
The cochlea can’t discern the difference between two closely spaced frequencies, especially as the frequencies increase.
The ear is able to discern both very quiet and very loud sounds of very small and very large frequencies – hence the ear hears logarithmically – for both power and frequency.
Notes: Cochlea – שבלול
להזכיר פיזיקה 1 – תדר רזוננס עולה יחד עם קבוע הקפיץ w0^2 = k/m
בקיצור – גם האוזן עושה ניתוח תדר
The coiled shape of the cochlea enhances lower frequency vibrations as they travel down the coil.

## Slide 17: What does the ear do?

## Slide 18: שאלות עד כאן?

## Slide 19: פיצ'רים לשמע

## Slide 20
מוטיבציה
נרצה להשיג מידע משמעותי (לחלץ פיצ'רים) מהאות המתקבל ובאמצעותו להסיק מסקנות על השמע ולאמן עליו מודלים שידעו לעשות דברים מעניינים.
* זוהי מצגת בלמ"ס אז את הדברים המעניינים תסיקו בעצמכם...

## Slide 21: מגל קול לאות דיגיטלי
מיקרופון ממיר את הגל האקוסטי למתח חשמלי (אות אנלוגי) שמומר לאות דיגיטלי ע"י דגימה. הפרמטר שמשפיע על רזולוציית האות הדיגיטלי הוא תדר הדגימה.
לפי תנאי נייקוויסט ניתן לשחזר תדרים הקטנים ממחצית תדר הדגימה. אם כן באילו תדרי דגימה משתמשים לשמע?

## Slide 22
אפשר להשיג מידע על השמע מהסתכלות על ה"גל הגולמי" (raw waveform):
הדגימות עצמן
ממוצע/סטיית תקן
אמפליטודה מקסימלית
מרחק בין מקסימות (זמן מחזור)
מספר חציות 0 (zero crossing rate)
ועוד...
זמן זה נחמד והכל, אבל בשביל מה דיברנו על תדרים?
פיצ'רים על הגל

## Slide 23: התמרת פורייה
התמרת פורייה ממירה את האות שלנו ממישור הזמן למישור התדר
  שימו לב – זוהי פונקציה מרוכבת – לכל תדר הערך הוא מספר מרוכב הבנוי ממגניטודה ופאזה.
Notes: Fourier Transform (FT): decomposes functions depending on space or time into functions depending on spatial frequency or temporal frequency.
Example plot of a speech sample, 1 kHz sinusoidal tone represented as a waveform, spectrogram.

## Slide 24: התמרת פורייה – בעולם הבדיד
במחשב האות מיוצג על ידי מספר סופי של דגימות בפרק זמן סופי, ולכן "הגרסה הפרקטית" של התמרת פורייה היא ה Discrete Fourier Transform (DFT)
Notes: Main goal of slide: Integrals are converted to sums in the digital/practical use case

## Slide 25: STFT
מכיוון שהאות בתוך מקטע שמע (שאורך מספר שניות) משתנה באופן תדיר, אנחנו נרצה מידע ספקטרלי ברזולוציה גבוהה יותר (עשרות מילישניות). לשם כך נעזר ב Short-time Fourier Transform (STFT)
Notes: Main goal of slide: Integrals are converted to sums in the digital/practical use case

## Slide 26: ספרקטרוגרמה
The spectrogram is the result of the magnitude squared of the STFT:
בגלל התפיסה הלוגריתמית של עוצמה – נהוג לעבוד עם הלוגריתם של הספקטרוגרמה.

## Slide 27
Voic‌ed
הפקה - לחץ האו‌ויר מתוך הריאות גורם לרטיטת מיתרי הקול.
במישור הת‌דר - Ρitch תדר בסיסי שחוזר / מסרק תדרים.
אנרגי‌ה - ריכוז בתדרים נמוכים, לרוב איזור נמוך מ 2KHz
Speech Spectrogram
ՍnVo‌iced
הפקה- מעב​ר אוויר ברווחים צרים,לא נוצרת רטיטה של מיתרי ​הקול.
במישור התדר - מאופייני‌ם בספקטרום רחב סרט בתדרים גבוהים.​
אנר​גיה - ריכוז בתדרים ג​בוהים, לרוב אזור גבוה מ 2KHz

## Slide 28
בדומה לפיצ'רים בסיסיים שניתן להשיג מהwaveform ניתן להשיג פיצ'רים בסיסיים מהספקטרוגרמה:
אמפליטודה/פאזה של הדגימות
Spectral centroid – התדר המשוקלל הממוצע בכל נקודת זמן
מדדי ניגודיות שונים (spectral bandwith)
ועוד... ראו librosa.feature.
פיצ'רים על הספקטרוגרמה

## Slide 29: Mel Scale
מכיוון שאנו תופסים תדרים בצורה לוגריתמית, אפשר להמיר את התדרים לסקלת מל מהרץ:

## Slide 30: Mel Filterbanks
Sounds like a feature!
לצורך חילוץ פיצ'רים מספקטרוגרמה נהוג להשתמש בmel filterbanks – אלה חלונות המרוחקים לינארית בסקלת מל ובהם מכפילים את הספקטרוגרמה.
נהוג להשתמש בעשרות פילטרים כאלה (whisper משתמש ב80)
Notes: Relate to last point regarding “Everything meaningful is usually up to 4000 Hz”

## Slide 31: Log-Mel-Filterbanks
Use the characteristics of speech and the cochlea to extract meaningful features:
Frame the signal into short frames (20-40ms)
Calculate DFT (discrete Fourier transform) for each frame.
  We have the spectrogram now.
Apply Mel Filters
Calculate logarithm of the filterbank energies.

## Slide 32: MFCC
Use the characteristics of speech and the cochlea to extract meaningful features:
Frame the signal into short frames (20-40ms)
Calculate DFT (discrete Fourier transform) for each frame.
  We have the spectrogram now.
Apply Mel Filters
Calculate logarithm of the filterbank energies.
  We have the log-mel-spectrogram now.
Apply DCT (discrete cosine transform, similar to FFT).
Only keep DCT coefficients 2-13.

## Slide 33: Final remarks on MFCC
The filterbanks are overlapping and thus resulting energies are correlating, the DCT decorrelates them.
The higher DCT coefficients represent fast changes in the frequency space, which aren’t relevant to speech recognition tasks.

## Slide 34: Speech Features in Practice
* You might use a different package in the exercise

## Slide 35: Speech Features in Practice
Waveform
Spectrogram
Log-Spectrogram
MFCC
MFCC[2:14]

## Slide 36: שאלות?

## Slide 37: ML

## Slide 38: Dimensionality Reduction
Problems in high-dimensional data:
  We can’t look on our data and get intuition about it 
  It might be difficult to make good models using it
There are many ways to reduce our data dimensions
  PCA/KPCA
  T-SNE
  UMAP
  …
Also the properties of data will effect the quality of the reduction:
  Centering
  Normalization
  Outliers
  …

## Slide 39: PCA (Principal Component Analysis)
An orthogonal projection of the onto lower dimensional linear space.
The subspace maximizes the variance of the projected data

## Slide 40: T-SNE
Non-linear dimensionality reduction method
T-SNE in practice:
from sklearn.manifold import TSNE reducer = TSNE(n_components=2) # to fit and transform: X_reduced = reducer.fit_transform(X)

## Slide 41: Embeddings
You might be interested in the embedding space – a space you project your data to
You can get insights about your data and model by exploring the embedding space

## Slide 42: CNN – Convolutional neural network

## Slide 43: Embeddings example – word2vec
After using PCA and reducing our data to 2D space we can found meaning in the most principal components:
X – name – capitol
Y – country related

## Slide 44: Transfer-Learning
It sometimes hard to train a NN from scratch
We can use pretrained NN and exploit its generalization properties for new tasks - It can save us a lot of time and resources!

## Slide 45: Transfer-Learning in practice

## Slide 46: SVM Support Vector Machine

## Slide 47: Linear Classifiers
f
x
yest
denotes +1
denotes -1
How would you classify this data?
Estimation:
w: weight vector
x: data vector
f(x,w,b) = sign(w. x + b)

## Slide 48: Linear Classifiers
f
x
a
yest
denotes +1
denotes -1
How would you classify this data?
f(x,w,b) = sign(w. x + b)

## Slide 49: Linear Classifiers
f
x
a
yest
denotes +1
denotes -1
How would you classify this data?
f(x,w,b) = sign(w. x + b)

## Slide 50: Linear Classifiers
f
x
a
yest
denotes +1
denotes -1
How would you classify this data?
f(x,w,b) = sign(w. x + b)

## Slide 51: Linear Classifiers
f
x
a
yest
denotes +1
denotes -1
Any of these would be fine..
..but which is best?
f(x,w,b) = sign(w. x + b)

## Slide 52: Classifier Margin
f
x
a
yest
denotes +1
denotes -1
Define the margin of a linear classifier as the width that the boundary could be increased by before hitting a datapoint.
f(x,w,b) = sign(w. x + b)

## Slide 53: Maximum Margin
f
x
a
yest
denotes +1
denotes -1
The maximum margin linear classifier is the linear classifier with the, um, maximum margin.
This is the simplest kind of SVM (Called an LSVM)
Linear SVM
f(x,w,b) = sign(w. x + b)

## Slide 54: Maximum Margin
f
x
a
yest
denotes +1
denotes -1
f(x,w,b) = sign(w. x + b)
The maximum margin linear classifier is the linear classifier with the, um, maximum margin.
This is the simplest kind of SVM (Called an LSVM)
Support Vectors are those datapoints that the margin pushes up against
Linear SVM

## Slide 55: Estimate the Margin
What is the distance expression for a point to a line ?
denotes +1
denotes -1
x
wx +b = 0
X – Vector
W – Normal Vector
b – Scale Value
W

## Slide 56: Large-margin Decision Boundary
The decision boundary should be as far away from the data of both classes as possible
  We should maximize the margin, m
  Distance between the origin and the line wtx=-b is b/||w||
Class 1
Class 2
m

## Slide 57: Finding the Decision Boundary
Let {x1, ..., xn} be our data set and let yi Î {1,-1} be the class label of xi
The decision boundary should classify all points correctly Þ
To see this: when y=-1, we wish (wx+b)<1, when y=1, we wish (wx+b)>1. For support vectors, we wish y(wx+b)=1.
The decision boundary can be found by solving the following constrained optimization problem

## Slide 58: Next step…
Allowing a few errors
  Soft margin
Converting SVM to a form we can solve
  Dual form
Allowing nonlinear boundary
  Kernel functions

## Slide 59: Allowing errors in our solutions
We allow “error” xi in classification; it is based on the output of the discriminant function wTx+b
xi approximates the number of misclassified samples
Class 1
Class 2

## Slide 60: Soft Margin Hyperplane
If we minimize åixi, xi can be computed by
  xi are “slack variables” in optimization
  Note that xi=0 if there is no error for xi
  xi is an upper bound of the number of errors
We want to minimize
  C : tradeoff parameter between error and margin
The optimization problem becomes

## Slide 61: The Dual Problem
This is a quadratic programming (QP) problem
  A global maximum of ai can always be found
w can be recovered by
Notes: נתעלם מאיך מגיעים לזה – קבלו כנתון

## Slide 62: Extension to Non-linear Decision Boundary
So far, we have only considered large-margin classifier with a linear decision boundary
How to generalize it to become nonlinear?
Key idea: transform xi to a higher dimensional space to “make life easier”
  Input space: the space the point xi are located
  Feature space: the space of f(xi) after transformation
Notes: XOR: x_1, x_2, and we want to transform to x_1^2, x_2^2, x_1 x_2
It can also be viewed as feature extraction from the feature vector x, but now we extract more feature than the number of features in x.

## Slide 63: Transforming the Data (c.f. DHS Ch. 5)
Computation in the feature space can be costly because it is high dimensional
  The feature space is typically infinite-dimensional!
The kernel trick comes to rescue
f( )
f( )
f( )
f( )
f( )
f( )
f( )
f( )
f(.)
f( )
f( )
f( )
f( )
f( )
f( )
f( )
f( )
f( )
f( )
Feature space
Input space
Note: feature space is of higher dimension than the input space in practice

## Slide 64: The Kernel Trick
Recall the SVM optimization problem
The data points only appear as inner product
As long as we can calculate the inner product in the feature space, we do not need the mapping explicitly
Many common geometric operations (angles, distances) can be expressed by inner products
Define the kernel function K by

## Slide 65: An Example for f(.) and K(.,.)
Suppose f(.) is given as follows
An inner product in the feature space is
So, if we define the kernel function as follows, there is no need to carry out f(.) explicitly
This use of kernel function to avoid carrying out f(.) explicitly is known as the kernel trick

## Slide 66
Non-linear SVMs: Feature spaces
General idea: the original input space can always be mapped to some higher-dimensional feature space where the training set is separable:
Φ: x → φ(x)

## Slide 67: Degree of Polynomial Features
X^1
X^2
X^3
X^4
X^5
X^6

## Slide 68: SVM in Practice
>>> from sklearn import svm
>>> clf = svm.SVC(kernel=‘rbf’)
>>> clf.fit(X, y)
# to predict on new samples:
>>> clf.predict(X_new)

## Slide 69: GAN (Generative Adversarial Network)

## Slide 70
Outline
GAN
  Random generator
  G(z) and D(x)
cGAN
Pix2pix
Cycle Consistency
CycleGAN
Notes: 70

## Slide 71
GAN (Ian Goodfellow et al., NIPS 2014)
Credit(modified from) https://www.slideshare.net/xavigiro/deep-learning-for-computer-vision-generative-models-and-adversarial-training-upc-2016
Real world samples
Generator
⃝ ⃝⃝
Discriminator
⃝ ----- ⃝
Loss
X
z
D
G(z)
D(x)
D(G(z))
Overview
Notes: 71

## Slide 72
GAN (Ian Goodfellow et al., NIPS 2014)
Credit(modified from) https://www.slideshare.net/xavigiro/deep-learning-for-computer-vision-generative-models-and-adversarial-training-upc-2016
Training Discriminator
Real world samples
(G)enerator
⃝ ⃝⃝
(D)iscriminator
⃝ ----- ⃝
Loss
X
z
P(G(z))
D(x, θd)
D(G(z), θg)
Pdata(x)
Pprior(z)
=
G(z)
Notes: 72

## Slide 73
GAN (Ian Goodfellow et al., NIPS 2014)
Credit(modified from) https://www.slideshare.net/xavigiro/deep-learning-for-computer-vision-generative-models-and-adversarial-training-upc-2016
Training Generator
Real world samples
(G)enerator
⃝ ⃝⃝
(D)iscriminator
⃝ ----- ⃝
Loss
X
z
P(G(z))
D(x, θd)
D(G(z), θg)
Pdata(x)
Pprior(z)
=
G(z)
Notes: 73

## Slide 74
GAN (Ian Goodfellow et al., NIPS 2014)
Value of
Minimize G
Maximize D
Expectation
Distribution of real data
Prob. Of D(real)
Distribution of generated samples
Prob. Of D(fake)
fake
Notes: 74

## Slide 75
Outline
GAN
cGAN
  Condition with some vector y
  G(x, y) and D(x, y)
Pix2pix
CycleGAN
Summary
Notes: 75

## Slide 76
cGAN (Mehdi et al., 2014)
Condition the GAN with some vector y.
See the networks with a probabilistic point of view.
Generator G(z, y)
  modeling the distribution of data given z and y
Discriminator D(x, y)
  Labels X and XG are modeled with d ~ D(d|X, y)
Objective function
Credit: https://arxiv.org/pdf/1411.1784.pdf
Notes: 76
y is a label.

## Slide 77
Outline
GAN
cGAN
Pix2pix
  z = x
  Paired image-to-image translator
  Adversarial is on image level
CycleGAN
Summary
Notes: 77

## Slide 78
pix2pix (Phillip Isola et al., CVPR 2017)
  Generator G(x) – generate the synthesized pair for given image x
  Discriminator D(<x, G(x)>)
  Paired
Credit: http://openaccess.thecvf.com/content_cvpr_2017/papers/Isola_Image-To-Image_Translation_With_CVPR_2017_paper.pdf
Notes: Pix2pix, an image-to-image translator
It is a cGAN, where the input of the Generator is real image rather than just some latent vector.
In this model, The Generator is trained to fool the discriminator, by generating some image in domain Y given some image in domain X. For example, mapping edges to photo, or mapping sketch to painting. The Discriminator is trained to classify between fake (the generated image) and the real (the input of the Generator) tuples. So, we can see that the adversarial is on image level in pix2pix.
78

## Slide 79
Outline
GAN
cGAN
Pix2pix
CycleGAN
  Architecture
  Cycle Consistency
  Implementation
  Results
  Limitations
Summary
Notes: 79

## Slide 80
CycleGAN – Architecture
Y
G: X -> Y
F: Y -> X
DY
DX
X
Cycle consistency loss
Cycle consistency loss
GAN (Y2X) loss
GAN (X2Y) loss
G
F
Notes: cycleGAN is a variant of GAN that learns the translation/conversion between two sets of data source, these two sets of data source (they called two domains) do not correspond to each other.
The networks contain two generators and two discriminators.
The generator G translates an image in domain X to an image in domain Y.
The discriminator Dy determines whether the input is from domain Y or is generated by the generator G.
And vice versa the generator F and the discriminator Dx.
80

## Slide 81
Cycle Consistency
Translator G: English -> Chinese
Translator F:
Chinese -> English
EN
EN’
CN
Cycle-consistency loss
Obviously, we expected
EN -> G(EN) -> F(G(EN)) ~ EN
Formalized,
if G: X -> Y, F: Y -> X; expect,
X -> G(X) -> F(G(X)) ~ X
CN
EN’
Notes: 81

## Slide 82
CycleGAN – Objective Function
Adversarial loss (for G: X -> Y)
Cycle-consistency loss
Credit: https://arxiv.org/pdf/1703.10593.pdf
Full objective
Aim to solve
Notes: Swapping X/x and Y/y can get the adversarial loss for F: Y -> X
Lgan(G, Dy, X, Y) – how much you can distinguish Y (an input) from the real Y and the generated Y with the discriminator Dy
Lgan(G, Dx, Y, X) – how much you can distinguish X (an input) from the real X and the generated X with the discriminator Dx
Lcyc(G, F) – distance between X and the re-constructed X (F(G(X))) + the distance between Y and the re-constructed Y (G(F(Y)))
82

## Slide 83
CycleGAN – Implement
Generator network
6 blocks for 128 x 128 images
  c7s1-32, d64, d128, R128, R128, R128, R128, R128, R128, u64, u32, c7s1-3
9 blocks for 256 x 256 and higher resolution images
  c7s1-32, d64, d128, R128, R128, R128, R128, R128, R128, R128, R128, R128, u64, u32, c7s1-3
Conv layer #2
Conv layer #1
Residual block #2
Residual block #1
Residual block #n
Conv layer #2
Conv layer #1
encoding
decoding
transforming
input
output
Notes: C7s1-k denote a 7x7 Convolution-InstanceNorm-ReLU layer with k filters and stride 1.
Dk denotes a 3x3 Convolution-InstanceNorm-ReLU layer with k filters and stride 2.
Reflection padding was used to reduce artifacts.
Rk denotes a residual block that contains two 3x3 convolutional layers with the same number of filters on both layer.
Uk denotes a 3x3 Fractional-Strided-Convolution-InstanceNorm-ReLU layer with k filters and stride ½.
83

## Slide 84
CycleGAN – Implementation
Discriminator network
70x70 PatchGAN
  c64, c128, c256, c512
Credit: https://affinelayer.com/pix2pix/
Notes: 84

## Slide 85
CycleGAN – Results
Notes: Check the paper
Images
Analysis
85

## Slide 86
CycleGAN – Limitations
https://qiita.com/itok_msi/items/b6b615bc28b1a720afd7#%E8%BF%BD%E5%8A%A0%E5%AE%9F%E9%A8%93%E7%B5%90%E6%9E%9C20170614%E8%BF%BD%E8%A8%987
Tasks require
geometric changes
Changes in distribution characteristics (test set vs. training set)
A lingering gap between the results achievable from pix2pix and that achieved by CycleGAN.
Notes: 86

## Slide 87
Outline
GAN
cGAN
Pix2pix
CycleGAN
Summary
Notes: 87

## Slide 88: Evaluation
FPR – false positive rate
TPR – true positive rate

## Slide 89: Evaluation
ROC (receiver operating characteristic) curve
Confusion Matrix

## Slide 90: Questions?